## Slide 1: Fast Packet Processing In Linux with AF_XDP
DPDK Summit Bangalore – March 2018
Magnus Karlsson and Björn Töpel, Intel
Presented by Nikhil Rao, Intel

## Slide 2: Motivation
Provide high performance packet processing integrated with upstream Linux kernel
User
Kernel
L2 Fwd
DPDK PMD
IGB_UIO
User
Kernel
L2 Fwd
DPDK PMD
i40e
Current Model
AF_XDP

## Slide 3: XDP Background
XDP – Programmable, High Performance Packet Processor in kernel data path

## Slide 4: Proposed Solution
AF_XDP socket
  Use XDP program to trigger Rx path for selected queue
DMA transfers use user space memory (Zero Copy)
  HW descriptors mapped to kernel
  Requires HW steering support
Copy-mode for non-modified drivers
Goal to hit 40 Gbit/s for large packets and 25 Gbit/s for 64 byte packets (37 Mpps) on a single core
Cores + NICs
SKB
Linux NIC Driver
Libc
New App
Stack
AF_INET
socket
Legacy App
AF_XDP
socket
Kernel
User Space
Modified Code
Un-modified Code
XDP

## Slide 5: Packet Path Rx (ZC)
Application
NIC
DMA
Interrupt Handler
softirq
EBPF
XDP_REDIRECT
ZC_RCV
Mmap’ed
Rx Ring
Mmap’ed
“Loan” Ring

## Slide 6: Operation Modes
  From slower -> faster
  XDP_SKB:
    Works on any netdevice using sockets and generic XDP path
  XDP_DRV:
    Works on any device with XDP support (all three NDOs)
  XDP_DRV + ZC:
    Need buffer allocator support in driver + a new NDO for TX

## Slide 7: NIC Driver Support (XDP_DRV + ZC)
ndo_bpf()
  Enable/Disable ZC commands { .., XSK_REGISTER_XSK, XSK_UNREGISTER_XSK }
ndo_xdp_xsk_xmit()
  Submit XDP packet when ZC is enabled
ndo_xdp_xsk_flush()
  Update NIC Tx queue tail pointer

## Slide 8: Security and Isolation for XDP_DRV + ZC
  Important properties:
    User space cannot crash kernel or other processes
    User space cannot read or write any kernel data
    User-space cannot read or write any packets from other processes unless packet buffer is explicitly shared
  Requirement for untrusted applications:
    HW packet steering, when there are packets with multiple destinations arriving on the same interface
    If not available => XDP_SKB or XDP_DRV mode need to be used

## Slide 9: DPDK Benefits
DPDK AF_XDP PMD
  No change to DPDK apps
  Linux handles hardware
  Goal: < 10% performance decrease
No need for SR-IOV bifurcated drivers
DPDK App1
Cores + NICs
DPDK App2
DPDK App3
Linux NIC Driver
Goal: Linux should be used for HW setup, DPDK used purely as a shared library

## Slide 10: Usage*
sfd = socket(PF_XDP, SOCK_RAW, 0);
buffs = calloc(num_buffs, FRAME_SIZE);
.. Pin memory with umem character device ...
setsockopt(sfd, SOL_XDP, XDP_RX_RING, &req, sizeof(req));
setsockopt(sfd, SOL_XDP, XDP_TX_RING, &req, sizeof(req));
mmap(..., sfd); /* map kernel Tx/Rx rings */
.. Post Rcv buffers ..
struct sockaddr_xdp addr = { PF_XDP, ifindex, queue_id };
bind(sfd, addr, sizeof(addr));
for (;;) {
read_messages(sfd, msgs, ....);
process_messages(msgs);
send_messages(sfd, msgs, ....);
};
*WIP

## Slide 11: Experimental Setup
  RFC V1 of AF_XDP published on January 31, 2018
  Broadwell E5-2699 v4 @ 2.10GHz
  2 cores used for benchmarks
  Rx is a softirq (thread)
  Tx is driven from application via syscall
    TX and RX is currently in same NAPI context
    Item in backlog to make this a thread on third core
  One VSI / queue pair used on I40E. 40Gbit/s interface
  Ixia load generator blasting at full 40 Gbit/s
App
Core 1
RX
TX
Core 2

## Slide 12: Performance I40E 64-Byte Packets
“Results have been estimated based on internal Intel analysis and are provided for informational purposes only. Any difference in system hardware or software design or configuration may affect actual performance. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more information go to http://www.intel.com/performance/datacenter.
 | AF_PACKET V3 | XDP_SKB | XDP_DRV | XDP_DRV + ZC
rxdrop | 0.73 Mpps | 3.3 Mpps | 11.6 Mpps | 16.9 Mpps
txpush | 0.98 Mpps | 2.2 Mpps | - | 21.8 Mpps
l2fwd | 0.71 Mpps | 1.7 Mpps | - | 10.3 Mpps
  XDP_SKB mode up to 5x faster than previous best on Linux
  XDP_DRV ~16x faster
  XDP_DRV + ZC up to ~22x faster
    Not optimized at all at this point!
    Rxdrop for AF_PACKET V4 in zero-copy mode was at 33.7 Mpps after some optimizations. We have more work to do.

## Slide 13: Future Work
  More performance optimization work
  Try it out on real workloads
  Make send syscall optional and get TX off RX core
  Packet steering using XDP
  Metadata support, using XDP meta_data
  Queue pairs w/o HW support gets emulated
  XDP redirect to other netdevices RX path
  1 XDP program per queue pair
  XDP support on TX
  Multi producer single consumer queues for AF_XDP
  Clone pkt configuration

## Slide 14: Conclusions
  Introduced AF_XDP
  Integrated with XDP
  AF_XDP with zero-copy provides up to 20x performance improvements compared to AF_PACKET V2 and V3 in our experiments on I40E NIC
  RFC on the netdev mailing list
  Still lots of performance optimization and design work to be performed
  Lots of exciting XDP extensions possibile in conjunction with AF_XDP
  Check out the RFC:
  https://patchwork.ozlabs.org/cover/867937/

## Slide 15: Acknowledgements
  Alexei Starovoitov, Alexander Duyck, John Fastabend, Willem de Bruijn, and Jepser Dangaard Brouer for all your feedback on the early RFCs
  Rami Rosen, Jeff Shaw, Ferruh Yigit, and Qi Zhang for your help with the code, performance results and the paper
  The developers of RDMA, DPDK, Netmap and PF_RING for the data path inspiration
  Check out the RFC:
  https://patchwork.ozlabs.org/cover/867937/

## Slide 16: Questions?